## Slide 1: EP8900 Integrated Assesment Modelling
SSP 4 for South Africa

## Slide 2: Assumptions for SSP4
1. Overall demand change - adjustement based on projection of GDP in the SSP database for SSP4: results in a decrease in demand
2. R&C demand: the speed of the transition from traditional biomass to electricity is slowed down
3. Rebound effect: as all energy prices become cheaper, the demand for all energgy categories is linearly increased to 15 % in 2070.
4. inv_cost: nuclear, solar and wind costs decreased in order to reach around 50% of SSP2 in 2100, 5% decrease per year
5. fix_cost: nuclear, solar and wind costs decreased in order to reach around 50% of SSP2 in 2100, 5% decrease per year
6.var_cost: biomass_non-commercial decreased at 10% in each year due to social increased acceptance (factor is based on expert knowledge;-) )
7.var_cost: extraction costs for all fuels decreased by 5% in each year due to lower labor costs

## Slide 3: Main drivers
Population is decreasing much faster than in the reference scenario

## Slide 4: Main drivers
The growth of GDP is lower than in the baseline scenario

## Slide 5: Results
GHG Emissions
The GHG emissions are lower compared to SSP2 due to the lower demand
Chart: GHG emissions ( MtCO2eq)
| 2020 | 2030 | 2040 | 2050 | 2060 | 2070
SSP2 | 527.5309 | 664.4814 | 744.6824 | 872.336 | 1046.9165 | 1284.7106
SSP4 | 527.6366 | 623.0373 | 676.3132 | 736.6381 | 828.5247 | 997.2725
SSP4_no_rebound | 523.2596 | 601.7266 | 639.1708 | 675.1856 | 738.7424 | 866.328

## Slide 6: Results
Growth of renewables
Chart: Renewable Energy (Gwa)
| 2020 | 2030 | 2040 | 2050 | 2060 | 2070
SSP2 | 18.4831 | 21.5934 | 23.1874 | 25.8976 | 26.3094 | 22.9515
SSP4 | 18.0806 | 22.9805 | 27.0084 | 36.3341 | 44.185 | 46.4282
SSP4_no_rebound | 16.657 | 21.7418 | 25.8021 | 35.1054 | 42.9188 | 46.2564
Renewables grow faster than in SSP2 after 2030. The rebound effect has little influence

## Slide 7: Results
Growth of renewables
Solar is decreasing, while wind is increasing. After 2050?
Chart: Wind Capacity (GW)
| 2020 | 2030 | 2040 | 2050 | 2060 | 2070
SSP2 | 2.3559 | 6.313 | 31.5231 | 90 | 31.8529 | 5.5532
SSP4 | 2.3559 | 21.3001 | 28.8235 | 90 | 60 | 10.4604
SSP4_no_rebound | 2.3559 | 20.2039 | 17.6322 | 90 | 59.0201 | 10.2895
Chart: Solar Capacity (GW)
| 2020 | 2030 | 2040 | 2050 | 2060 | 2070
SSP2 | 18.4575 | 6.4357 | 2.244 | 0.7848 | 0.18243 | 0.031804
SSP4 | 4.6896 | 1.6352 | 0.57014 | 0.20116 | 0.04676 | 0.0081521
SSP4_no_rebound | 4.6896 | 1.6352 | 0.57014 | 0.20116 | 0.04676 | 0.0081521

## Slide 8: Results
Nuclear
Less nuclear than in SSP2. More without rebound effect?
Chart: Electricity - Nuclear (Gwa)
| 2020 | 2030 | 2040 | 2050 | 2060 | 2070
SSP2 | 3.0743 | 1.0719 | 0.37376 | 0.097743 | 0.02272 | 0.0039611
SSP4 | 0.59136 | 0.20619 | 0.071896 | 0.018801 | 0.0043704 | 0.00076194
SSP4_no_rebound | 0 | 0 | 0.86112 | 0.22519 | 0.052346 | 0.009126

## Slide 9: Results
Fossil fuel capacity
Fossil capacity increases a lot after 2040.
Chart: Gas Capacity (Gwa)
| 2020 | 2030 | 2040 | 2050 | 2060 | 2070
SSP2 | 58.0762 | 67.8458 | 38.9386 | 110.2074 | 79.0748 | 27.9521
SSP4 | 51.4098 | 52.7899 | 29.7397 | 92.5183 | 65.7891 | 21.2156
SSP4_no_rebound | 50.2934 | 49.6194 | 24.4984 | 87.1164 | 60.0044 | 18.9071
Chart: Coal Capacity (Gwa)
| 2020 | 2030 | 2040 | 2050 | 2060 | 2070
SSP2 | 93.4354 | 65.1634 | 59.5359 | 128.7185 | 74.6652 | 43.8013
SSP4 | 92.5942 | 44.2262 | 40.825 | 95.736 | 37.5539 | 29.4117
SSP4_no_rebound | 90.1665 | 40.3439 | 39.261 | 87.8222 | 31.7119 | 26.2755

## Slide 10: Results
Coal Extraction
Coal extraction going up, but less than in SSP2. Most of the rebound effect is coal…
Chart: Coal Extraction (GWa)
| 2020 | 2030 | 2040 | 2050 | 2060 | 2070
SSP2 | 194 | 225.4441 | 239.6454 | 271.4802 | 322.6325 | 401.017
SSP4 | 194 | 211.9068 | 217.8495 | 229.4223 | 256.1194 | 314.6416
SSP4_no_rebound | 193.3436 | 206.965 | 208.9746 | 214.2519 | 233.6235 | 279.3157

## Slide 11: Results
Evolution of the electricity mix
2020

## Slide 12: Results
Evolution of the electricity mix
2030

## Slide 13: Results
Evolution of the electricity mix
2040

## Slide 14: Results
Evolution of the electricity mix
2050

## Slide 15: Results
Evolution of the electricity mix
2070
Chart: 
| SSP2 | SSP4 | SSP4_no_rebound
Coal | 43.8013 | 29.4117 | 26.2755
Gas | 27.9521 | 21.2156 | 18.9071
Hydro | 3.8564e-05 | 3.8564e-05 | 3.8564e-05
Nuclear | 0.0039611 | 0.00076194 | 0.009126
CCS | 0.002694 | 0.0022872 | 0.0019209
Solar | 0.031804 | 0.0081521 | 0.0081521
Wind | 5.5532 | 10.4604 | 10.2895